## Slide 1: Automatic Brain Tumor Detection and Segmentation Using U-Net Based Fully Convolutional Networks
JooHyun Lee

## Slide 2: BraTS
Multimodal Brain Tumor Segmentation Challenge
Challenge: https://www.smir.ch/BRATS/Start2016
Data Link: http://medicaldecathlon.com
Dataset:
Modality: Multimodal multisite MRI data (FLAIR, T1, T1c, T2)
Label: Background / Necrotic and Non-enhancing tumor / Edema / Enhancing tumor
Size: 750, 4D Volumes (484 training + 266 Testing) / (Image Size: 240×240×155×4)
Source: BRATS 2016 and 2017 Dataset
< Multimodal MRI data >

## Slide 3: Label / Target
Label
Label 0: Background
Label 1: Necrotic and non-enhancing tumor
Label 2: Edema
Label 3: Enhancing Tumor
Target
Complete: Label 1 + Label 2 + Label 3
Core: Label 1 + Label 3
Enhancing: Label 3
Prediction (Segmentation)
FLAIR → Complete
FLAIR → Core
T1c → Enhancing

## Slide 4: Data Preprocess
Data Augmentation
< Original Data > < Augmented Data >

## Slide 5: Model
U-Net
< U-Net Diagram >

## Slide 6: Train
Loss: Dice Coefficient
The dice coefficient D between two binary volumes can be written as
where the sums run over the N voxels, of the predicted binary segmentation volume pi ∈ P and the ground truth binary volume gi ∈ G.
Optimizer: Adam (learning rate=0.0001)
Train: 5 - Cross Validation
Initialization: Weights: Normal Distribution (mean: 0, standard deviation: 0.01)
Biases: Initialized as 0
Device: GTX 1080 Ti 4 ways + Intel i7-7700K
< Training Capture >

## Slide 7: Tricks
Data Imbalance Solution
Problem
Dataset ratio (pixel-level)
1) Normal ( > 98.5% )
2) Abnormal ( < 1.5%)
In spite of using ‘Dice Coefficient Loss’, it was impossible to train using whole dataset without any tricks
Solution
30% Image slides ( Abnormal pixel ratio > 5% )
70% Image slides ( Abnormal pixel ratio < 5% )

## Slide 8: Tricks
Noise Reduction
Erosion
< Original Image > < After Erosion >

## Slide 9: Tricks
Threshold Tuning
Recall vs. Precision
1. Maximization Recall (Threshold ↓ )
ex) HIV Home Testing Kit (Recall 99.9%)
< HIV Home Testing Kit >
2. Maximization Precision (Threshold ↑ )
ex) Criminal Detection Camera
< Criminal Detection Camera >

## Slide 10: Results
Image Ground-Truth Prediction
Complete
Core
< Brain MRI (FLAIR) Segmentations >
DSC |  |  |  |  | 
Method | Data | Grade | Complete | Core | Enhancing
Mine | Cross-Validation on BRATS 2016-2017 Training Datasets | Combined | 0.87 | 0.84 | - (0.50)
Paper | Cross-Validation on BRATS 2015 Training Datasets | Combined | 0.86 | 0.86 | 0.65

## Slide 11: Results (3D Images)
Complete
Ground Truth Prediction
< Complete Segmentations using Brain MRI (FLAIR) >
Core
Ground Truth Prediction
< Core Segmentation using Brain MRI (FLAIR>
Use Slide-Show to watch 3D Images

## Slide 12
Data Imbalance
Data Imbalance on “Enhancing Dataset” (0.1% on pixel level)
Unable to train ‘Enhancing’ Model
→ Brain Mask for balancing data
→ Use Multimodal MRI inputs
< Pill Mask > < After removing edges >
Models
- Conv vs. Astrous Conv
- Deconv vs. Upsample vs. No-Decoding
- SOTA Models
< Comparison with state-of-the-art semantic segmentation network >
Discussion

## Slide 13: Code
Github
Code was uploaded in https://github.com/JooHyun-Lee/BraTs

## Slide 14: Reference
[1] Hao Dong, Guang Yang , Fangde Liu , Yuanhan Mo , Yike Guo.: Automatic Brain Tumor Detection and Segmentation
Using U-Net Based Fully Convolutional Networks
[2] Milletari, F., Navab, N., Ahmadi, S.-A.: V-Net: Fully Convolutional Neural Networks for Volumetric Medical Image Segmentation